## Slide 1: BTEC NAT – UNIT 27 NETWORKING OSI MODEL
Unit Leader: Dave Bell
david.bell@castlecollege.ac.uk

## Slide 2: THE OSI 7 LAYER MODEL
Open Systems Interconnection
A standard description or “reference model” for how messages should be transmitted between any two points in a telecommunication network
Any two computers can communicate when connected regardless of underlying architecture

## Slide 3
The OSI 7 Layer Model
Application layer
Presentation layer
Session layer
Transport layer
Network layer
Data Link layer
Physical layer
User services, application, activities
Actual data transmission communications subnet

## Slide 4: THE OSI SEVEN LAYER MODEL
UPPER 4 LEVELS
message passing – from computer to computer
LOWER 3 LEVELS
message passing – through host computer to another
PURPOSE
to separate specific functions

## Slide 5: APPLICATION LAYER 7
Interacts with applications for communication purposes
Determines identity & availability of communications partners
Determines sufficient resources available
Controls the communication -
cooperation between applications

## Slide 6: PRESENTATION LAYER 6
Presents data to the user in understandable format
Provides conversion functions for application layer data
Data representation – graphic formats
Character representation – text / ASCII
Data compression Data encryption

## Slide 7: SESSION LAYER 5
Manages connections between machines
Determines whether all data transmitted / received
Establishes logical connection for communication
Checks data received – retransmits if necessary
Reconnects on premature termination
Releases logical connection on completion

## Slide 8: TRANSPORT LAYER 4
Decides upon network to use depending on data type
Flow control – enough space to send/receive messages
Multiplexing – combines messages to same connection
Packeting – breaks larger into smaller pieces
Error checking and recovery
Firewalls, Security & Prioritisation

## Slide 9: NETWORK LAYER 3
Routing and addressing functions – correct destinations
Receives incoming packets of data
IP – IP addresses
Routing – decides what route to use
Forwarding – sends on packets to other hosts
Controls communication subnet – layers 1-3

## Slide 10: DATA LINK LAYER 2
Organisation of data bits into frame structure
MAC Addresses (NICs) – identify devices
NICs, Switches, WAN Technologies
The beginning and end of the data frame
The address of the sender
The address of the receiver
Error checking of the data frame

## Slide 11: PHYSICAL LAYER 1
Transmits / receives data bits as electrical pulses
Controls physical link between communicating systems
Describes network topology
Transmission media – cabling / broadcasting / wireless
Modems – encoding binary bit of data
Electrical or optical (fibre optic) signalling

## Slide 12: TCP / IP
Basic communication protocol of the Internet
TRANSMISSION CONTROL PROTOCOL
Manages assembly of messages / files into smaller packets. Reassembles packets when received (OSI layer 4)
INTERNET PROTOCOL
Handles the address part of the packet
Ensures reaches correct destination (OSI layer 3)

## Slide 13: TCP / IP (4 Layer)

## Slide 14: TCP / IP Protocols
OSI LAYERS | TCP LAYERS | PROTOCOLS
Application | Application | FTP Telnet HTTP POP3 SMTP TFTP HTTPS
Presentation |  | 
Session |  | DNS
Transport | Transport | TCP UDP
Network | Internet | IP ICMP OSPF EIGRP BGP RIP HSRP DHCP
Data Link | Data Flow or Network Access layer | ARP RARP
Physical |  |